V V

LED500WCMYCTO Three in one head head lamp

Instructions for use

(RDM, color display)

catalogue

Chapter 1. Notes and Installation	1

1. Maintenance	1

. 2 statement	1

3. Product precautions	1

4. Installation of lamps and lanterns	1

Chapter 2. Panel Operation	3

1. Overview	3

2. Operation	3

1. Operate lamps with intuitive touch or auxiliary input (touch support products)	3

2. Parameter numerical input	3

3. Set the options on / off	4

4. Subpage (parameter)	4

3. Functional operation and parameter setting	4

1. Set the DMX address code	4

2. Set up the working mode of the lamps	5

3. Panel display settings	6

4. Scene mode	7

5. Set the working parameters of the lamps	8

6. Check the current status of the lamp	9

Chapter 3: Channel description	11

1. Channel table	11

Chapter 4. Common faults and use attention	14

1. Common fault handling	14

2. Notes for use	15

3. Notes for the use of RDM	15

Notes and installation

tending

- This lamp shall be kept dry to avoid working in a wet environment.

- Intermittent use will effectively prolong the life of this lamp.

- In order to achieve good ventilation and lighting effects, pay attention to regularly clean the fans, fan nets and lenses.

- Do not wipe the lamp shell with organic solvents such as alcohol to avoid damage.

statement

This product in the factory, the performance of intact, complete packaging. All users shall strictly comply with the warnings and operating instructions stated above, any damage caused by misuse is not covered by the Company's warranty and the faults and problems caused by the neglect of the operating manual.

This manual is subject to technical changes without prior notice.

Precautions for products

- In order to ensure the service life of the product, the product should not be placed in a wet or leaky place, nor to work in the temperature above 60 degrees

- Do not place the product in a place that is easy to loosen or vibrate.

- In order to avoid the danger of electric shock, this product.

- When the bulb is used, the voltage change of the power supply should not exceed ± 10%. If the voltage is too high, it will shorten the life of the bulb. If the voltage is too low, it will affect the light color of the bulb.

- After power failure, it takes 20 minutes to use the lamp to cool adequately before energizing again.

- To ensure the normal use of this product, please read the instructions carefully.

- Signal line connection (DMX)

Use specification compliant RS-485 cable: with shielding, 120 ohm characteristic impedance, 22-24 AWG, low tolerance. Do not use microphone cables or cables with different specified characteristics. The terminals must have a 3-or 5-pin XLR male / female connector. Figure 1 shows the schematic diagram of the signal line connection (the lamp in the figure is an example picture and does not represent the true appearance of the product).

Important: The ines shall not contact each other or with the metal shell.

Figure 1 Schematic diagram of the DMX signal line connection

Lighting installation

Lamps can be placed horizontally, oblique and upside down. We must pay attention to the installation method when hanging in oblique and inverted hanging.

As shown in figure 2, (the lamps and lanterns as the example picture, does not represent the true appearance of the product) before the lamps, to ensure the stability of the installation site, in the reverse hanging installation, must ensure not fall on the support frame, need to use safety rope through the support frame and lamps handle for auxiliary hanging, to ensure safety, prevent the lamps and lanterns from falling and sliding.

When the lamps are installed and tested, pedestrians are not allowed to pass below. Regularly check whether the safety rope is worn and whether the hook screws are loose.

Our company shall not bear any responsibility for all the consequences caused by the unstable installation of the hanging and the lamp falling.

Figure 2 Schematic diagram of the inverted lamp

Panel operation

  - summary

The schematic diagram of the lamp panel is shown in Figure 3, the upper left corner of the title is the number of lamp channels, the black font shows the lamp fault status (when the fault information is not viewed, display "E RR", otherwise "NOR"), the current lamp signal, bulb status, communication status (the panel is the example picture, which does not represent the real outside of the product panel, please select the panel of the same type for reference).

This lamp supports DMX / RDM. Agreement, when the lamp is searched by the RDM host, three letters "RDM" will appear in the panel, indicating that the lamp is enumerated normally.

Note: Do not use sharp or sharp display to prevent damage.

Display the panel schematic diagram

operate

Operating lamps with visual touch or auxiliary input (touch)

- The left area is the TFT display area and touch area. Click the content of the panel with fingers or blunt surface hardware, or the parameter setting or view status can be completed.

- The right area is the auxiliary input. If the touch function without TFT, you can use the auxiliary input to select the items to be set or viewed to complete the operation.

- For the knob shown in Figure 3-3, the cursor can be controlled up or down, and pressing the knob can confirm. If you want to return, rotate the knob to move the cursor to the position of the return key on the display, press the knob to confirm to return.

Parameter numerical input

When the selected parameter item needs to enter a numerical value, the window opens as shown in Figure 4:

Figure 4 Numerical setting page

- Set the value: you can directly pull the slider to quickly set the required value, or click the "up" or "down" button on the right to accurately set the required value or set it with auxiliary input.

- Save the value: at any time, click the "OK" key in the lower right corner, that is, save the current value to the internal memory, the next boot to have the saved value applied to the lamp.

Set the options on / off

- When the set parameter is on / off, directly click the corresponding item to switch the parameter value, which will be saved to the internal memory. Press the parameter option on the right, and the corresponding option turns gray. When releasing the hand, the corresponding parameters are changed and saved.

- The determination of important parameters is be by the validation window, as shown in Figure 5 below:

Figure 5. Confirm the input window

Subpage (parameter)

Functional operation and parameter setting

Enter the Settings interface, as shown in Figure 6-1:

- In the main interface, you can enter the corresponding parameter setting interface by selecting six buttons.

- In the parameter setting interface, you can press the left blue option to quickly switch to the other setting interfaces.

    - Set up the DMX address code

The DMX address and channel mode of the lamp can be set on the page shown in Figure 6-1 below.

graph 6-1

The menu setting of the lamp optimizes the setting of the address, and the address code operation is as follows:

- Select "Last" or "Next", the lamp will automatically calculate the address code of the next or last one according to the current address code and channel data, which can be quickly set up;

- Click the address code value to enter the value editing window, where any valid address code can be set, the lamp can automatically obtain the current number of channels of the lamp, and automatically filter the unusable address code (512-current number of channels).

- The lamp supports the RDM protocol, and the lamp address code can be set remotely through the RDM.

Provide two push-buttons:

- Channel mode: different channel modes can be selected periodically;

- Lamp reset: reset all motors.

Set up the lamp working mode

graph 6-2

Set the operation mode of the lamp and control the bulb through the page as shown in Figure 6-2 above. The lamp supports four operating modes (DMX mode, self-driven mode, voice control mode and scene mode). Please refer to the previous section for detailed parameter value setting. Specific parameter descriptions are shown in the following table:

running mode

| DMX pattern | Console mode, receive the DMX signal, the RDM signal |
| --- | --- |
| Self-walking mode | The lamp runs automatically according to the built-in program |
| Sound control mode | When the lamp detects a strong sound, the lamp automatically runs a scene according to the built-in program, otherwise maintain the last scene |
| Scene mode: 01 | Run as a set scene, and support custom editing for up to 10 scenes |
|  | 1~10 | Outputs the specified scene |
|  | voluntarily | Automatically output the scene in the set scene time (non-0) order, and the scene with time 0 is automatically skipped and ignored |
| Master from choice | When the non-DMX mode works, select the data output mode, the lamp automatically detects the DMX state and automatically switch the output to prevent data conflict |
|  | main engine | The lamp runs as built-in, if DMX has no signal, output data (synchronization), otherwise no data output |
|  | slave | Lamlamp operate as built-in, no output data (not synchronized with other lamps) |
|  | voluntarily | If the DMX has no signal, the lamp operates as built in, otherwise, the lamp works with the DMX signal |
| Light bulb switch | (Bulb source) pop confirmation dialog box, select "SURE" to confirm the current operation, open or close the bulb, switch time interval limited to 30 seconds |
|  | close | The current bulb output is already turned off |
|  | open | The current light output is already turned on |

Scene mode is suitable for a single or a small number of lamps, only output a fixed scene, or need to run a simple program, can be edited in the scene page without connecting the console.

If the light source is a bulb, wait 10 minutes before turning the bulb turned off.

Panel display settings

graph 6-3

The lamps support Both Chinese and English, inverted display, etc. Enter the corresponding parameter setting as shown in Figure 6-3. The specific menu contents are shown in the following table:

Display settings

| language | Set up the language of the display |
| --- | --- |
|  | English | English display |
|  | the Chinese language | Chinese display |
| Screen protection | Set the display content or mode of the screen after the screen has no operation within 30 seconds |
|  | close | Keep the last operation page, and light up the screen |
|  | pattern 1 | Out of the screen |
|  | pattern 2 | Black screen, showing the address code of the current lamp in the lower left corner |
|  | pattern 3 | Displays the trademark information, address code and operation mode |
|  | pattern 4 | Display trademark information, address code and operation mode, extinguish for 30 seconds |
| Screen rotation | Set the display direction of the screen |
|  | close | No reversal is shown |
|  | open | Reverse display |
|  | voluntarily | Automatically detect the direction of lamp and automatically switch the display direction |
| DMX indicate | Set the indication mode of the DMX signal indicator light |
|  | pattern 1 | When the signal is bright, when there is no signal, go out |
|  | pattern 2 | Out when signal, bright when no signal |
|  | pattern 3 | Blink when signal, extinguish when no signal |
| The signal indicates brightness | Set the brightness of the signal indicator light |
|  | 1~10 | Ten grades |
| Screen backlight | Set the brightness of the screen backlight after 10 seconds of no operation, full bright during operation |
|  | 1~10 | Ten grades |
| Touch screen switch | Select whether to disable the touch screen. When the screen touch is accidentally damaged, please disable the touch function and set the lamp with auxiliary input |
| Touch correction | When the screen touch is not accurate, you can enter the correction page correction screen |

Lamps that support touch operation. If a bad touch phenomenon occurs, you can enter the correction page to recorrect the touch accuracy of the touch screen. Under normal circumstances, please do not enter this page. If the touch is damaged, select to disable the touch switch.

Scene mode

Enter the page shown in Figure 6-4 below (the channel shown in the picture is only an example to introduce the function, please refer to the channel table in the following section for the specific channel table), and the lamp enters the scene editing mode. Under this page, when the [console mode] option is closed, the lamp does not receive the DMX console data to the lamp. When opened, receive the console signal and read the console data to the corresponding channel display.

graph 6-4

The content of the page depends on the currently selected channel, and the channel content and order displayed are consistent with the lamp channel table. Through this page, 10 scenes can be edited, as shown in the following table:

Scene mode

| Scenario selection | Select the current required action scenario |
| --- | --- |
|  | 1~10 | 10 scenarios |
| Scene time | Set the retention time of the current scene in the automatic time, and the final time is determined by the multiple of the scene time in 0.1 seconds |
|  | 0 | The current scene does not participate in the automatic scene output |
|  | 1-255 | From 0.1 seconds to 25.5 seconds |
| Control platform mode | Select whether to use the console to control the setting data |
|  | close | Unable to use the console control, directly set up the data in the current interface |
|  | open | Use console control, setting with console data first, in the current interface setting is invalid |
| 1. X axis | 0-255 | Set the data of each channel, the display content and sequence correspond to the channel table of the lamp |
| …… | 0-255 |  |
| …… | 0-255 |  |
| N.function | 0-255 |  |

If the effective reset data is edited in the reset channel in the scene, the lamp will reset, but after reset, the value of the corresponding reset channel will automatically reset to prevent multiple consecutive reset.

On this page, you can get the current channel table order of the lamp. Please refer to the detailed channel description for the specific channel data.

Set the working parameters of the lamp

graph 6-5

Enter the page shown in Figure 6-5 above, adjust the field parameters of the lamps, and facilitate the field installation of the lamps, etc.:

advanced setup

| X axis reverse | Set the X-axis rotation direction |
| --- | --- |
|  | close | Don't reverse |
|  | open | opposite direction |
| Y axis reverse | Set the Y-axis rotation direction |
|  | close | Don't reverse |
|  | open | opposite direction |
| Optical coupling correction | Set whether the lamp detects XY misstep and correct |
|  | close | Position is not corrected after the misstep |
|  | open | Automatic correct the position after the lost step and record the lost step fault |
| X-axis offset | Set the position of the lamp |
|  | 4-150 |  |
| Y axis offset | Set the position of the Y axis of the lamp |
|  | 4-48 |  |
| data-hold | Set the output status of the lamp when the lamp has no DMX signal |
|  | close | There is no signal, so the motor and the light source return to the position and state when the reset is complete |
|  | open | No signal, keeping the last frame of the DMX data output |
| Scene time multiple | Work together with the scene time to determine the scene retention time |
|  | 1-255 | Retention time = scene time * multiple |
| Turn on the light mode | Set the way the bulb is turned on for the first time |
|  | Turn on the light | Turn on the bulb first when powered on, and reset the lamp after 30 seconds |
|  | Turn on the light after reset | Reduce the lamp for 3 seconds, and turn the bulb on after the reset |
|  | Turn on the light manually | After the reset, manually open the bulb through the menu or console |
| Factory setting | The confirmation box pops up. After selecting "SURE", the lamp parameters return to the factory settings |

When choosing the power opening bubble mode, the lamp will wait for the bulb for 30 seconds after powering on, so that the bulb can fully start. After the internal voltage is stable enough, then start the reset program. If the field power capacitance is stable, it is recommended to start the bulb mode.

When the lamp cannot correct the position, first check whether the optical coupling correction is closed.

When the signal is removed, if the lamp position is not output as intended, check the Data Hold setting first.

When setting the XY offset, after completing the setting, please control the XY with the maximum stroke to check the setting, XY will not hit the positioning rod or shell.

View the current status of the lamp

graph 6-6

Entering the page shown in Figure 6-6, you can view the information and real-time status of the lamps to know the use status of the lamps. If the lamps need an after-sales service, please provide the status information displayed on the page as the judgment basis, as shown in the following table:

status information

| Motor information | Display the information status of all motors and signals in the lamp |
| --- | --- |
|  | Hoare | Not shown, it means that the motor is not Hall corrected, 0 means that the motor leaves the correction position point, and 1 means that the motor is at the correction position point |
|  | state | Show the motor reset completion state |
|  | X axle | Displays the real-time position value of the X-axis optical coupling feedback |
|  | Y axle | Display the real-time position value of the Y-axis optical coupling feedback |
|  | optocoupler | Show the level state of two signals with X and Y axis, binary |
| Fault / status record | Display the last 8 fault records of lamp reset and operation, the fault records are not saved after power failure, when the next power cycle is valid |
|  | fault data | Total number of faults detected after power-on |
|  | 12：:03 | Power time in minutes |
|  | Hall fault | The corresponding motor does not detect an effective Hall signal when the motor is reset |
|  | Hall short circuit | The Hall signal of the motor detected at the corresponding motor reset is always valid |
|  | Optical coupling failure | No effective photocoupling signal is detected when the corresponding motor is reset |
|  | fall out step | The corresponding motor loses its step during operation |
|  | Crash rod | Cragainst the positioning lever when the motor is reset |
|  | Bulb failure | Light bulb accidentally extinguished |
|  | Sensor failure | Temperature sensor signal is abnormal |
|  | Fan fault | The main fan is not working properly |
| Lighting status | Displays the critical status data for the current lamp for reference |
|  | communication | 0~100%, the communication quality of the data link within the lamp |
|  | miscount | The number of error frames detected after power, accumulated |
|  | Light source temperature | Show the temperature of the current light source, "- - -" indicates no detection |
|  | Display plate temperature | Displays the temperature of the current display board or the nearby ambient temperature |
|  | Sensor 1 temperature | Displays the current motherboard temperature or the ambient temperature at the motherboard installation location |
| Version information | Display the information and version of current lamps and make an important reference for after-sales maintenance |
|  | equipment | Name of lamp, same to equipment information of RDM |
|  | model | Model of lamp, same as model information of RDM |
|  | display board | Firmware version and serial number of the display board |
|  | Main board 1 | Firmware version and serial number of the motherboard 1 |
| Light source time | Record the total accumulative time of the light source, as a reference for regular maintenance of the light source |
| Lamps time | Record the total cumulative time of lamp opening, unit minutes, do not clear |

Channel description

  - channel table

Note: different lamp channel table varies, the following channel table is for reference only

The lamp channel can be viewed in scene mode. The channel mode is set in the Address Settings page. The detailed data are shown in the following table below:

channel table

| channel 1 | channel 2 | name | numeric value |
| --- | --- | --- | --- |
| [ CH1 ] | [ CH1 ] | X axle | 0-255 |
| [ CH2 ] | [ CH2 ] | X axis fine-tuning | 0-255 |
| [ CH3 ] | [ CH3 ] | Y axle | 0-255 |
| [ CH4 ] | [ CH4 ] | Y axis fine-tuning | 0-255 |
| [ CH5 ] |  | XY velocity | 0-255 |
| [ CH6 ] | [ CH5 ] | aiming | 0-255 |
| [ CH7 ] | [ CH6 ] | stroboflash |  |
|  |  |  | 0-3 |
|  |  |  | 4-103 |
|  |  |  | 104-107 |
|  |  |  | 108-155 |
|  |  |  | 156-207 |
|  |  |  | 208-212 |
|  |  |  | 213-251 |
|  |  |  | 252-255 |
| [ CH8 ] | [ CH7 ] | colour disk |  |
|  |  |  | 0-9 |
|  |  |  | 10-19 |
|  |  |  | 20-29 |
|  |  |  | 30-39 |
|  |  |  | 40-49 |
|  |  |  | 50-59 |
|  |  |  | 60-69 |
|  |  |  | 70-79 |
|  |  |  | 80-89 |
|  |  |  | 90-99 |
|  |  |  | 100-109 |
|  |  |  | 110-119 |
|  |  |  | 120-129 |
|  |  |  | 130-139 |
|  |  |  | 140-149 |
|  |  |  | 150-159 |
|  |  |  | 160-169 |
|  |  |  | 170-179 |
|  |  |  | 180-215 |
|  |  |  | 216-220 |
|  |  |  | 221-255 |
| [ CH9 ] | [ CH8 ] | ching | 0-255 |
| [ CH10 ] | [ CH9 ] | pinkish red | 0-255 |
| [ CH11 ] | [ CH10 ] | yellow | 0-255 |
| [ CH12 ] | [ CH11 ] | CTO | 0-255 |
| [ CH13 ] | [ CH12 ] | The dial |  |
|  |  |  | 0-4 |
|  |  |  | 5-9 |
|  |  |  | 10-14 |
|  |  |  | 15-19 |
|  |  |  | 20-24 |
|  |  |  | 25-29 |
|  |  |  | 30-34 |
|  |  |  | 35-39 |
|  |  |  | 40-44 |
|  |  |  | 45-49 |
|  |  |  | 50-54 |
|  |  |  | 55-59 |
|  |  |  | 60-64 |
|  |  |  | 65-69 |
|  |  |  | 70-74 |
|  |  |  | 75-79 |
|  |  |  | 80-84 |
|  |  |  | 85-89 |
|  |  |  | 90-94 |
| [ CH14 ] | [ CH13 ] | Rotation dial |  |  |  |
|  |  |  | 0-9 | white light |  |
|  |  |  | 10-19 | Pattern 1 |  |
|  |  |  | 20-29 | Pattern 2 |  |
|  |  |  | 30-39 | Pattern 3 |  |
|  |  |  | 40-49 | Pattern 4 |  |
|  |  |  | 50-59 | Pattern 5 |  |
|  |  |  | 60-69 | Pattern 6 |  |
|  |  |  | 70-79 | Pattern 7 |  |
|  |  |  | 80-89 | From slow to fast jitter pattern 1 |  |
|  |  |  | 90-99 | From slow to fast jitter pattern 2 |  |
|  |  |  | 100-109 | From slow to fast jitter pattern 3 |  |
|  |  |  | 110-119 | From slow to fast jitter pattern 4 |  |
|  |  |  | 120-129 | From slow to fast jitter pattern 5 |  |
|  |  |  | 130-139 | From slow to fast jitter pattern 6 |  |
|  |  |  | 140-149 | From slow to fast jitter pattern 7 |  |
|  |  |  | 150-200 | From fast to slow forward flowing water |  |
|  |  |  | 201-205 | cease |  |
|  |  |  | 206-255 | From slow to fast, the reverse flow of water |  |
| [ CH15 ] | [ CH14 ] | Disc rotation |  |  |  |
|  |  |  | 0-127 | 0-360 degrees |  |
|  |  |  | 128-190 | From fast to slow reverse flow water |  |
|  |  |  | 191-192 | cease |  |
|  |  |  | 193-255 | From slow to fast forward flowing water |  |
| [ CH16 ] |  | Illustre fine-tuning | 0-255 |  |  |
| [ CH17 ] | [ CH15 ] | Prism 1 |  |  |  |
|  |  |  | 0-127 | not have |  |
|  |  |  | 128-255 | Insert prism 1 |  |
| [ CH18 ] | [ CH16 ] | Prism rotation |  |  |  |
|  |  |  | 0-127 | 0-360 degrees |  |
|  |  |  | 128-187 | From fast to slow forward flowing water |  |
|  |  |  | 188-195 | cease |  |
|  |  |  | 196-255 | From slow to fast, the reverse flow of water |  |
| [ CH19 ] | [ CH17 ] | Prism 2 |  |  |  |
|  |  |  | 0-127 | not have |  |
|  |  |  | 128-255 | Insert prism 2 |  |
| [ CH20 ] | [ CH18 ] | Prism 2 rotation |  |  |  |
|  |  |  | 0-127 | 0-360 degrees |  |
|  |  |  | 128-187 | From fast to slow forward flowing water |  |
|  |  |  | 188-195 | cease |  |
|  |  |  | 196-255 | From slow to fast, the reverse flow of water |  |
| [ CH21 ] | [ CH19 ] | atomization |  |  |  |
|  |  |  | 0-127 | not have |  |
|  |  |  | 128-255 | atomization |  |
| [ CH22 ] |  | great | 0-255 |  |  |
|  |  |  | 0-15 | not have |  |
|  |  |  | 16-255 | great |  |
| [ CH23 ] | [ CH20 ] | amplify | 0-255 | down to |  |
| [ CH24 ] | [ CH21 ] | focus | 0-255 | From far to near |  |
| [ CH25 ] |  | Focus tuning | 0-255 |  |  |
| [ CH26 ] |  | great |  |  |  |
|  |  |  | 0-127 | not have |  |
|  |  |  | 128-255 |  |  |
| [ CH27 ] | [ CH22 ] | Reduction / function |  |  |  |
|  |  |  | 0-209 | NF |  |
|  |  |  | 210-215 | Reset the XY motor after 3 seconds |  |
|  |  |  | 216-219 | NF |  |
|  |  |  | 220-235 | Return the effect motor after 3 seconds |  |
|  |  |  | 236-239 | NF |  |
|  |  |  | 240-255 | Return to the whole lamp after 3 seconds |  |

Color temperature: 7500K color display index: 75 input voltage: AC90V-240V / 50-60 HZ

Light source specification: ECO350-80-R00-000

Light source life: 20,000 hours

lumen illumination: 4 m 120000 lm

Out light diameter: 138MM

Rated power: 600W

Channel mode: 22 / 27 channel

Horizontal scan: 540 degrees (16bit precision scan) electronic error correction

Vertical scan: 270 degrees (16bit precision scan) electronic error correction

Dimming system: 0-100% linearity

Focal system: 4 m to 50 m

Abulization system: 1 independent atomization effect, soft and natural light spot

Scale angle: the beam is 2.7-40° staining 4-40° pattern 4-40 °

High-speed strobe: 0-30 times / second. Adjustable speed strobe effect. Flash macro function

Color: 8 colors + white light. Color semi-color function

Color system: independent CMY + CTO mixed color system.

Fixed pattern: 12 fixed patterns + white light

Rotary pattern: 7 glass patterns, each glass pattern can be reversed and reversed independently

Prism system: standard single 6 row prism and 8 prism, each prism can be independent forward and reverse

Macro function: console reset function, self-go mode, master-slave mode

Display mode: LCD display, button + touch double operation mode

Control signal: international standard DMX512. With RDM function, can be online software upgrade, dial the address code

Cooling mode: use the axial fan to strengthen the cooling

Safety device: with electronic temperature control overheating protection, electronic temperature control automatic power failure protection

Appearance material: high-temperature resistant plastic

Working environment: -20 degrees, 40 degrees

Protection level: IP20

Product net weight: 22.5KG

Product size: 38 * 27 * 65CM (L * W * H)

Paper pack size: 54 * 45 * 61CM

The total weight is 25KG

Air box one with two dimensions: 73 * 50 * 88CM

The total weight is 77KG